## Slide 1: SAFRAN engineering services programming under DO178 - 332

## Slide 2
DO-178 Overview

## Slide 3: DO-178 Overview
    DO-178 - Software Considerations in Airborne Systems and Equipment Certification
    Standard of RTCA Incorporation (in Europe it is ED-12B and standard of EUROCAE)
    Represents the avionics industry consensus to ensure software safety
    Acceptable by FAA and EASA certification authorities
    "The FAA and the civil aviation community recognize RTCA’S DO-178B as an acceptable means of compliance to the FAA regulations for SW aspects of certification."

## Slide 4: Software Levels in DO-178
Different failure conditions require different software conditions -> 5 levels

## Slide 5: Examples DO-178 Safety Levels
Safety-critical Levels C&D
  Anti-missile defense
  Data mining
  Health monitoring
  Mission planning and implementation
  Mission simulation and training
  Network-centric operation
  Real-time data recording and analysis
  Self-healing communication networks
  Telemetry
  Weapons targeting
Safety-critical Levels A&B
  Fly-by-wire controls
  Auto-pilot
  Air-traffic Separation Control
  Glass Cockpit Information Display
  Radar
  Jet Engine Control
  IFF (friend or foe)
  Missile guidance
  Missile launch
  Missile self-destruct

## Slide 6: Objectives for Safety Levels
Different levels of safety requires different objectives to be fulfilled
Defined by some tables in ANNEX A
Example: Table A-6 Objective 3.

## Slide 7
SW Development

## Slide 8: The plans
Five different plans:
  SW Development Plan
  SW Verification Plan
  SW Quality Assurance Plan
  SW Configuration Plan
  SW Aspects of Certification
Verification, management, quality assurance and certification are overlaid on the defined development process

## Slide 9: Software Planning
SW development standards
    SW requirements standard
      Language to be used (Plain English…)
    SW design standards
      Complexity limits, exclusion of recursion, dynamic memory allocation
    SW Code standards
      Syntax, semantics and constraints

## Slide 10: SW Development
High-Level requirements
    Based on system analysis and safety assessment
    Black-box view of the software component
    System level considerations
    Functional requirements by mode of operation
    Performance criteria
    Timing requirements
    Memory size constraints
    HW and SW interfaces

## Slide 11: SW Development
Low-Level requirements and Software Architecture
    SW requirements
    Derived from High-Level requirements
    Design constraints
      Task allocation
      Algorithms
      Data Structures
    Input/output definitions
    Data and Control flows
    Resource management and scheduling
    Design Methods

## Slide 12: SW Development
    Source Code
      Usually collection of “high-level” language and assembly
      Includes linker files, compile commands etc.
    Executable
      Completely target computer specific
      “machine readable”
    Final output is the integrated system on the target platform
      Cf. DO254

## Slide 13
Traceability &
Verification

## Slide 14: Traceability
    Through the complete product life-cycle (30+ years)
    From requirements to byte code (Level A)
    Essential for maintainability
    Back-annotation of errors
    Typical implementation:
      Excel
      Doors
      PTC Integrity
    Code generators usually gives extensive support
    Hard in case of multiple development tools

## Slide 15: Verification
    Two purposes
      Demonstrate intended function
      Demonstrate (to the extent possible) the absence of unintended function
    Consists of
      Reviews
      Analysis
      Testing
    The FAA or EASA representative needs to accept all part of the verification process. (e.g., test cases)
    Certification has legal issues : the developer is responsible!

## Slide 16: Verification
Reviews:
    Qualitative assessment of the process or product
    Typical implementation: checklist
    Applied on all SW Development process step (HLR, LLR, SW Arch., SW Coding, Test cases, etc.)
Analysis:
    Provide repeatable evidence of correctness
    Typical implementation: timing, stack analysis, data flow and call-tree

## Slide 17: Verification – Testing
Testing:

## Slide 18: Verification – Testing
    Structural Coverage
      Determine what software structure were not exercised
    Levels:
      Statement Coverage
      Decision Coverage
      Modified Decision / Condition Coverage (MC/DC)
        Each decision tries every possible outcome
        Each condition in a decision takes on every possible outcome
        Each entry and exit point is invoked
        Each condition in a decision is shown to independently affect the outcome of the decision
    Gaps
      Complier induced code (e.g., array bound checks)
      Deactivated code
      Dead code
    Performed on source code,
      except Level A
        Correspondence must be shown
        Complier optimization can introduce new code
    In addition, coverage of data and control coupling is required

## Slide 19: Verification – Testing examples (1/3)

## Slide 20: Verification – Testing examples (1/3)

## Slide 21: Verification – Testing examples (1/3)

## Slide 22: Verification – Testing examples (2/3)

## Slide 23: Verification – Testing examples (2/3)

## Slide 24: Verification – Testing examples (3/3)

## Slide 25: Verification – Testing examples (3/3)

## Slide 26
Annexes

## Slide 27: DO-330 - Software Tool Qualification Considerations
    Tools can introduce errors into the final system.
      Especialy, SW development tools.
    They are verified on the same level as the developed application.
    The DO-330 « Software Tool Qualification Considerations » specifies 3 qualified tools categories and 5 TQL.
      Corresponding more or less to DAL.
    E.g., Scade Suite, Matlab Stateflow, Wind River Diab compiler

## Slide 28: DO-331 - Model-Based Development and Verification Supplement to DO-178
Use of models for source code synthesis and verification
Early model based validation
Matlab Simulink (already used), AADL

## Slide 29: DO-332 - Object-Oriented Technology and Related Techniques Supplement
Oversees the OOP related techniques, including:
    parametric polymorphism
    Overloading
    type conversion
    exception management
    dynamic memory management
    Virtualization
Liskov Substitution Principle

## Slide 30: DO-333 - Formal Methods Supplement
Already used in many projects
Mature technologies available
Defines how certification credits can be earned by its use
Can be part of the Development process
Typical tools:
    Model checker
    Static code analyzers
    Theorem provers (only in limited scenarios)